## Slide 1: NUMERICAL EVALUATOR OF DYNAMIC RESPONSES OF SINGLE/MULTIPLE DEGREE(S) OF FREEDOM STRUCTURES
BY: KEVIN YONGCHUL KIM
Presented: May 21st, 2015

## Slide 2: Overview
Numerical Evaluator
  Complementary Learning Module
  Two sets of MATLAB based programs
    Single Degree of Freedom System (SDOF)
    Multiple Degrees of Freedom System (MDOF)
  USER INPUTS:
    Structural Properties (i.e. mass, stiffness, damping ratio)
    Forcing Functions or Earthquake Acceleration Data
  OUTPUTS
    Plots of Forcing Functions
    Plots of Displacements vs. Time
    Animation of Given Structure’s Response

## Slide 3: Single-Degree-of-Freedom Model

## Slide 4: To Run SDOF Program
Step #1: ENTER values into User_Input.m
Step #2: ENTER values into Forcing_Function.m
Step #3: RUN Project_Begin.m

## Slide 5: Step #1: Fill Up User_Input.m
Step #1: User_Input.m
  Define mass m, damping ratio ξ, stiffness k, initial conditions
  Select Numerical Analysis Type
    Central Difference Method
    Newmark’s Method
    Runge-Kutta Method
  Decide time step ∆t and time range
  State the Type of Forcing Function
    ‘1’ for Recorded Ground Motion
    ‘2’ for Theoretical Forcing Function

## Slide 6: Step #2: Fill up ForcingFunction.m
Create a force vector p(t)
Option #1: Theoretical Forcing Function
  Sample Forcing Input #1: Harmonic Function
User Defines:
Option #2: Feed Recorded Ground Motion
  Sample Forcing Input #2: El Centro EQ

## Slide 7: Step #3: Run Project_Begin.m
Output will display
Creates intermediary variables and vectors
  Time vector [t]
  Natural frequency, damping coefficient, natural period
Runs Numerical Analysis Method of User’s Choice
  Central Difference Method
  Newmark’s Method
  Runge-Kutta Method

## Slide 8: Central Difference Method
finite difference approximation of the time derivatives of displacement (i.e.velocity, acceleration)

## Slide 9: Central Difference Method Coded

## Slide 10: Newmark’s Method
Method based entirely on acceleration
Initial Variables
Iterative Steps
Attaining Responses

## Slide 11: Newmark’s Method Coded

## Slide 12: Runge-Kutta 4th Order Method
Uses weighted average of four individual slopes to attain slopes for displacement and velocity to increase by for a given time step

## Slide 13: Runge-Kutta 4th order in Matlab

## Slide 14: Plots and Animations
After any of the above iteration methods
  Position vector [u] matching time vector [t] is created.
  Outputs three subplots

## Slide 15: Theoretic Forcing Function

## Slide 16: Ground Motion

## Slide 17: SDOF Flowchart

## Slide 18: Multiple-Degrees-of-Freedom Overview
Equation of Motion turns into vectors and matrices
Modal frequencies and mode shapes attained.
Uncoupled matrices attained
Modal coordinates, [q], [q’], [q”] attained by numerical analysis similarly to u, u’,u” attained in SDOF case.
Real Displacements Attained by multiplying mode shapes by modal coordinates

## Slide 19: MDOF Model
Reinforced-Concrete Chimney Model
  Idealized as lumped mass cantilever
User specifies:
  Height of chimney
  # of nodes
  Stiffness of columns
  Masses of each nodes
  Damping ratio of the first two modes.
  Forcing Function incurred at each node
  OR
  Recorded Ground Motion

## Slide 20: To Run MDOF Program
Step #1: ENTER values into User_Input_MDOF.m
Step #2: ENTER values into MDOF_ForcingFunction.m
Step #3: RUN MDOF_Run.m

## Slide 21: Step #1:User_Input_MDOF.m
User specifies:
  Structural Properties
  Initial conditions of every node
  Specify Forcing Function
    1:ground motion
    2:theoretic function
  Select Analysis Type
  Select time step, time range
  User implicitly specifies # of nodes!

## Slide 22: Step #2: Fill up MDOF_ForcingFunction.m
Creates stacks force vectors [p(t)]
Option #1: Theoretical Forcing Function
  Sample Forcing Input #1: Step force at top story
Option #2: Feed Recorded Ground Motion
  Sample Forcing Input #2: El Centro EQ

## Slide 23: Step #3: Run MDOF_Run.m
Output will display
  Creates intermediary matrices
    Mass Matrix [m]: Diagonal matrix where mii=mi
    Statically condensed stiffness matrix
    Modal frequencies vector [ arranged in ascending order
      Mode Shape Matrix [] : each column::each modal freq.
    Rayleigh Damping Matrix [c]
    Create uncoupled matrices [M], [C], [K]

## Slide 24: Central Difference Method-MDOF
All scalar equations of SDOF Central Difference Method become matrix equations
  Add’l features:
    Transform modal coordinates to nodal displacements
    Invert matrices at certain steps
SDOF
MDOF

## Slide 25: CDM-Initial Calculations
Initial calculations:
u->[q];m->[M]; c->[C]; k->[K]

## Slide 26: CDM Iterations:

## Slide 27: Newmark’s Method—MDOF
Equations of Incremental equilibrium in SDOF Newmark’s Method
  Now Matrix Equations
Average Acceleration Method
  Unconditionally stable
Linear Acceleration Method
  Stable when dt < 0.551 Tj
    Where j is the amount of modes included in analysis.
    Otherwise solution blows up, giving meaningless results.

## Slide 28: Newmark’s Method Initial Calculations

## Slide 29: Newmark’s Method Iterations

## Slide 30: MDOF Plots and Animations
After any of the above iteration methods
  Modal coordinate matrix [q], Position matrix [u] matching length of time vector [t] are created
  Outputs a set of three plots

## Slide 31: Theoretic: Step Force 1000k @ Top on 5th story

## Slide 32: EQ: El Centro—4-story chimney

## Slide 33: Power Spectral Density Plot
Fast Fourier Transform
  Converts periodic functions as functions of its frequency and amplitude
  Produces complex numbers
Power Spectral Density Function
  Gets the norm of complex numbers
  Allows plotting: Amplitude’s variance along frequency
Optional User Input

## Slide 34: Power Spectral Density Plot: Free Vibration w. initial displacement at top degree-of-freedom

## Slide 35: Power Spectral Density Plot: El Centro EQ

## Slide 36: Flowchart MDOF Program

## Slide 37: Learning Module Exercise:
Find (by hand or program) the modal frequencies and mode shapes of a chimney idealized as a 3-degrees-of-freedom system as shown.
Enter each mode shapes into the initial displacement conditions under script User_Input_MDOF.m, and set it to free-vibration under script MDOF_ForcingFunction.m
Comment on what you observe in terms of modal frequencies, mode shapes, modal coordinates and actual displacements.
EI

## Slide 38: Exercise Continued
Modal Frequencies w1,w2,w3, with corresponding mode shapes
EI
(rad/s)

## Slide 39: Free Vibration: Initial Disp.=Mode Shape 1

## Slide 40: Free Vibration: Initial Disp.=Mode Shape 3

## Slide 41: Conclusion
Presented Walkthroughs of SDOF/MDOF Analysis Programs
  User Inputs
  Forcing Functions
  Numerical Analysis
  Plots
  Animations
  Fast Fourier Transform
Displayed Potential for its use as learning module
  Video demo for lecture
  Input-Output Program for verification
  Homework Ex. for understanding all relations of MDOF natural frequencies, mode shapes, modal coordinates, real displacements